### Table of Contents
1. Introduction
  1. Overview of the Case Study
  2. Objectives of the Network Simulation
  3. Scope of the Report
2. Network Design Requirements
  1. IP Addressing Scheme (192.168.200.0/23)
  2. Branch and Departmental Allocation
    1. Accounts: 59 Devices
    2. Administrator: 69 Devices
    3. Marketing: 119 Devices
    4. Sales: 249 Devices
3. Network Topology
  1. Design Considerations
  2. Network Layout and Structure (with diagrams)
  3. Device and Hardware Specifications
4. Subnetting
  1. IP Address Distribution
  2. Subnet Mask Calculation for Each Department
  3. Example Calculations
5. Configuration of Devices
  1. Router and Switch Configuration
  2. VLAN Configuration for Department Segmentation
  3. IP Assignment and DHCP Configuration
6. Simulation and Implementation
  1. Setup in Cisco Packet Tracer
  2. Steps for Creating the Network
  3. Testing Connectivity
7. Demonstration and Presentation
  1. Explanation of the Working Solution
  2. Key Features and Functionality Demonstrated
8. Challenges and Solutions
  1. Issues Faced During Simulation
  2. Solutions to Identified Problems
9. Conclusion
  1. Summary of the Solution
  2. Lessons Learned
10. References
  1. Tools and Software Used
  2. Sources for Additional Research

---
## 1. Introduction
### Overview of the Case Study
This report details the design and simulation of a network infrastructure for an organization that consists of three branches, each containing multiple departments: Accounts, Administration, Marketing, and Sales. The IP address block 192.168.200.0/23 has been assigned, and the organization requires the allocation of IP addresses and network resources to support 496 devices across these departments. The case study necessitates the development of a scalable, secure, and efficient network, implemented using Cisco Packet Tracer, to simulate the required topology.
The network simulation demonstrates how different departments, ranging in size from 59 to 249 devices, will be isolated using VLANs (Virtual Local Area Networks) and interconnected through routers and switches for optimal traffic management. The design is aimed at meeting both the current requirements and allowing for future expansion, ensuring that each branch and department can communicate securely within its own VLAN and across the entire network.
### Objectives of the Network Simulation
The main objective of this network simulation is to provide a detailed design and implementation that addresses the following key goals:
1. Departmental Segmentation: Using VLANs to segment network traffic, ensuring that each department operates within its isolated environment.
2. Inter-VLAN Communication: Enabling communication between departments and branches through inter-VLAN routing while maintaining security.
3. IP Addressing: Efficient distribution of IP addresses based on department size and ensuring there is enough address space for each department within the 192.168.200.0/23 subnet.
4. Network Scalability: Designing the network with scalability in mind, allowing easy expansion of departments or branches without major network overhauls.
5. Simulation and Testing: Simulating the network in Cisco Packet Tracer, verifying the correctness of the design through connectivity tests, and addressing potential issues such as VLAN trunking and routing.
6. Documentation and Presentation: Producing a detailed report and a presentation to explain the design choices, configurations, and the overall performance of the simulated network.
### Scope of the Report
This report will cover the complete process of designing and simulating the network architecture for the organization. It will provide a thorough analysis of:
- IP Addressing Scheme: Subnetting and IP allocation for different departments based on their device counts.
- Network Topology: The physical and logical layout of the network, including the placement of switches, routers, and connections between them.
- Device Configuration: Configuration of routers and switches, including VLAN creation, trunking, and inter-VLAN routing.
- Testing and Simulation: The process of testing the network’s functionality, ensuring that devices in each department can communicate with each other and with other branches.
- Challenges and Solutions: Addressing any technical difficulties encountered during the simulation process, such as VLAN misconfigurations or routing issues, and providing solutions.
- Conclusion and Lessons Learned: A summary of the overall design, simulation results, and lessons learned throughout the project.
---

## 2. Network Design Requirements
### IP Addressing Scheme (192.168.200.0/23)
The organization has been allocated the IP address range 192.168.200.0/23, which provides a total of 510 usable IP addresses. This address block is large enough to accommodate the current device count across all branches and departments while allowing room for future expansion.
The /23 subnet mask (255.255.254.0) provides 512 IP addresses, with the first and last addresses reserved for the network and broadcast addresses, respectively. This leaves 510 usable IP addresses for allocation across the four departments: Accounts, Administrator, Marketing, and Sales. The IP address space will be divided efficiently among the departments, with each department receiving a sufficient number of IP addresses to accommodate their current devices, and additional addresses reserved for scalability.
### Branch and Departmental Allocation
The network is segmented into multiple Virtual Local Area Networks (VLANs), with each department allocated a dedicated VLAN. This ensures network segmentation, security, and improved traffic management. The following allocation has been made based on the device count in each department:
#### Accounts: 59 Devices
- VLAN 10 is assigned to the Accounts Department, which consists of 59 devices.
- The subnet allocated for this department is 192.168.200.0/25, providing 126 usable IP addresses. This allows for the required 59 devices while leaving room for future growth.
- The range of IP addresses for this department will be from 192.168.200.1 to 192.168.200.126.
#### Administrator: 69 Devices
- VLAN 20 is assigned to the Administrator Department, which consists of 69 devices.
- The subnet allocated for this department is 192.168.200.128/25, which also provides 126 usable IP addresses.
- The range of IP addresses for this department will be from 192.168.200.129 to 192.168.200.254.
#### Marketing: 119 Devices
- VLAN 30 is assigned to the Marketing Department, with a total of 119 devices.
- The subnet allocated for this department is 192.168.201.0/25, providing 126 usable IP addresses, which meets the current requirement of 119 devices and leaves room for minor expansion.
- The IP address range for this department will be from 192.168.201.1 to 192.168.201.126.
#### Sales: 249 Devices
- VLAN 40 is assigned to the Sales Department, which consists of 249 devices.
- The subnet allocated for this department is 192.168.201.128/24, which provides 256 usable IP addresses, more than sufficient to accommodate the 249 devices.
- The range of IP addresses for the Sales department will be from 192.168.201.129 to 192.168.202.254.
### Summary of IP Allocation
The table below summarizes the IP allocation for each department, ensuring that each has enough address space to meet current and future needs:
Department	VLAN	Subnet	Usable IP Addresses	Device Count	IP Address Range
Accounts	VLAN 10	192.168.200.0/25	126	59	192.168.200.1 - 192.168.200.126
Administrator	VLAN 20	192.168.200.128/25	126	69	192.168.200.129 - 192.168.200.254
Marketing	VLAN 30	192.168.201.0/25	126	119	192.168.201.1 - 192.168.201.126
Sales	VLAN 40	192.168.201.128/24	256	249	192.168.201.129 - 192.168.202.254

This IP addressing scheme ensures that each department has sufficient IP address space, meets the requirement for segmentation using VLANs, and supports future expansion.

---

## 3. Network Topology
### Design Considerations
The design is based on a two-tier architecture, which combines the functionality of the core and distribution layers into a single layer while maintaining a separate access layer. This approach simplifies the network, reduces complexity, and offers a more cost-effective and efficient design, especially for medium-sized networks. The following considerations were taken into account:
1. Simplification of Architecture: The two-tier architecture eliminates the need for a separate distribution layer, making the network more straightforward while still maintaining efficient routing, security, and scalability.
2. Scalability: The two-tier model allows for easy expansion by adding more access layer switches and devices as needed. The network can support the current number of devices and can easily be scaled up for future growth.
3. Segmentation and Security: Each department is assigned its own VLAN, isolating traffic and ensuring that each department’s network traffic remains secure and manageable.
4. Performance: The core layer is responsible for routing between VLANs, while the access layer connects end devices to the network. This separation allows for optimized performance and better traffic management, reducing bottlenecks.
5. Redundancy: The core layer ensures redundancy through high-speed links, preventing single points of failure. Trunk links between switches ensure that VLAN traffic can flow between departments without disruption.
6. Cost Efficiency: By combining the core and distribution layers into one, the design reduces the number of devices needed, making it more cost-effective without sacrificing performance or scalability.

### Network Layout and Structure (with Diagrams)
The network follows a two-tier architecture model, with two layers: the core layer (which combines core and distribution functions) and the access layer. The core layer switch handles inter-VLAN routing, high-speed traffic forwarding, and traffic aggregation from the access layer switches.
#### Core Layer
- The core layer is responsible for high-speed data transfer and inter-VLAN routing across departments. It aggregates traffic from all access layer switches and ensures that traffic is forwarded efficiently across the network.
- The core layer switch also handles inter-department and inter-branch traffic, ensuring that VLANs are properly routed and that policies such as QoS and ACLs are enforced.
#### Access Layer
- The access layer connects end devices, such as PCs, printers, and phones, to the network. Each access layer switch is assigned a specific VLAN for each department (Accounts, Administrator, Marketing, and Sales).
- The access switches forward VLAN traffic to the core switch, where inter-VLAN routing is handled. Trunk links are used between the access and core switches to allow multiple VLANs to pass through a single physical connection.
#### Diagram: Two-Tier Network Topology
Below is a visual representation of the network’s two-tier architecture. The diagram illustrates how the core switch handles both routing and aggregation while access switches connect directly to end devices within each department.

[Insert your updated network diagram here]

### Device and Hardware Specifications
To implement this two-tier network design, the following hardware was used:
#### Core Layer:
- Cisco Catalyst 3650-PS24 (Core Switch):
  - Purpose: Serves as the core switch responsible for routing and traffic aggregation from the access layer.
  - Key Features:
    - 24 Gigabit Ethernet ports.
    - Layer 3 routing capabilities (RIP, OSPF, EIGRP).
    - Supports VLAN trunking and redundancy protocols (STP, EtherChannel).
    - Handles inter-VLAN routing for the entire network.
#### Access Layer:
- Cisco Catalyst 2960-24TT (Access Switches):
  - Purpose: Connects end devices in each department and forwards VLAN traffic to the core switch via trunk links.
  - Key Features:
    - 24 Fast Ethernet ports.
    - Layer 2 switching capabilities (VLAN tagging and segmentation).
    - Supports trunk ports for connection to the core switch.
    - Provides port security and basic QoS features for end devices.
#### End Devices:
PCs, Printers, and Phones: Each department is equipped with the necessary end devices, connected to the access layer switches. Each device is assigned an IP address from its respective VLAN and subnet.

---
## 4. Subnetting
### IP Address Distribution
The allocated IP address range for the network is 192.168.200.0/23, which provides a total of 512 IP addresses (510 usable IPs after accounting for the network and broadcast addresses). This range is sufficient to meet the organization's current requirements, as well as allowing room for future expansion.
Each department in the organization is allocated its own VLAN, and the IP address space is divided among these VLANs based on the number of devices in each department. The subnetting is designed to ensure efficient use of IP addresses, with room for growth in each department.
#### IP Address Distribution by Department:
- Accounts Department: 59 devices
  - Allocated IP Range: 192.168.200.0/25
  - Usable IP Addresses: 126 (from 192.168.200.1 to 192.168.200.126)
- Administrator Department: 69 devices
  - Allocated IP Range: 192.168.200.128/25
  - Usable IP Addresses: 126 (from 192.168.200.129 to 192.168.200.254)
- Marketing Department: 119 devices
  - Allocated IP Range: 192.168.201.0/25
  - Usable IP Addresses: 126 (from 192.168.201.1 to 192.168.201.126)
- Sales Department: 249 devices
  - Allocated IP Range: 192.168.201.128/24
  - Usable IP Addresses: 256 (from 192.168.201.129 to 192.168.202.254)
### Subnet Mask Calculation for Each Department
Each department is allocated a different subnet based on the number of devices it supports. The subnet mask is calculated based on the number of required IP addresses for each department.
#### Subnet Mask Calculation Process
The formula for calculating the number of usable IP addresses based on the subnet mask is:  IP Addresses of host bitsUsable IP Addresses=(2number of host bits)−2 (The "-2" accounts for the network and broadcast addresses, which cannot be assigned to devices.)
1. Accounts Department (59 Devices):
  1. Required IP addresses: 59
  2. We need at least 59 usable IP addresses, and the closest subnet that provides this many IPs is /25.
  3. A /25 subnet mask gives 126 usable IP addresses.
  4. Subnet Mask: 255.255.255.128
2. Administrator Department (69 Devices):
  1. Required IP addresses: 69
  2. A /25 subnet mask is used, which provides 126 usable IP addresses.
  3. Subnet Mask: 255.255.255.128
3. Marketing Department (119 Devices):
  1. Required IP addresses: 119
  2. A /25 subnet mask is used, which provides 126 usable IP addresses.
  3. Subnet Mask: 255.255.255.128
4. Sales Department (249 Devices):
  1. Required IP addresses: 249
  2. A /24 subnet mask is needed to provide at least 249 usable IP addresses.
  3. A /24 subnet provides 256 usable IP addresses.
  4. Subnet Mask: 255.255.255.0

### Example Calculations
Here’s a detailed breakdown of how the subnetting was calculated for each department:
#### 1. Accounts Department:
- Number of Devices: 59
- Required IP Addresses: At least 59.
- The closest subnet size that accommodates 59 devices is /25, which provides 126 usable IPs.
Subnet Calculation:
- Subnet Mask: /25 = 255.255.255.128
- Total IP addresses in /25:  total IP addresses232−25=27=128 total IP addresses
  - 2 addresses reserved (network and broadcast), so:
  usable IP addresses128−2=126 usable IP addresses
- Subnet Range: 192.168.200.0/25
  - Usable IP range: 192.168.200.1 to 192.168.200.126
#### 2. Administrator Department:
- Number of Devices: 69
- Required IP Addresses: At least 69.
- The closest subnet size that accommodates 69 devices is /25, which provides 126 usable IPs.
Subnet Calculation:
- Subnet Mask: /25 = 255.255.255.128
- Total IP addresses in /25:  total IP addresses232−25=27=128 total IP addresses
  - 2 addresses reserved (network and broadcast), so:
  usable IP addresses128−2=126 usable IP addresses
- Subnet Range: 192.168.200.128/25
  - Usable IP range: 192.168.200.129 to 192.168.200.254
#### 3. Marketing Department:
- Number of Devices: 119
- Required IP Addresses: At least 119.
- The closest subnet size that accommodates 119 devices is /25, which provides 126 usable IPs.
Subnet Calculation:
- Subnet Mask: /25 = 255.255.255.128
- Total IP addresses in /25:  total IP addresses232−25=27=128 total IP addresses
  - 2 addresses reserved (network and broadcast), so:
  usable IP addresses128−2=126 usable IP addresses
- Subnet Range: 192.168.201.0/25
  - Usable IP range: 192.168.201.1 to 192.168.201.126
#### 4. Sales Department:
- Number of Devices: 249
- Required IP Addresses: At least 249.
- The closest subnet size that accommodates 249 devices is /24, which provides 256 usable IPs.
Subnet Calculation:
- Subnet Mask: /24 = 255.255.255.0
- Total IP addresses in /24:  total IP addresses232−24=28=256 total IP addresses
  - 2 addresses reserved (network and broadcast), so:
  usable IP addresses256−2=254 usable IP addresses
- Subnet Range: 192.168.201.128/24
  - Usable IP range: 192.168.201.129 to 192.168.202.254
---